## Slide 1: NAME-338 Ship Design Project & Presentation
Supervised by,
Dr. N. M. Golam Zakaria
Professor,
Dept. of NAME,
BUET.
Presented by,
Touseef Hasan
Student ID: 1812044,
Mehedi Hasan
Student ID: 1712046.

## Slide 2
Owner’s Requirements
Vessel Type: Bulk Carrier
Capacity: 2300 tonnes
Service Speed: 10 knots
Route: Dhaka – Chittagong (Inland)
Route Distance: 315 km (171 nautical miles)

## Slide 3
Principal Particulars
Length Overall
Length between Perpendiculars
Breadth Mld.
Depth Mld.
Draft
Service Speed
CB
: 76.4 m
: 74.4 m
: 13.54 m
: 5.1 m
: 3.85 m
: 10 knots
: 0.79

## Slide 4
List of Contents
Scantling Calculations
Midship Section Drawing
Longitudinal Construction Drawing
Shell Expansion Drawing

## Slide 5
Scantling Calculations
Reference Book: Germanischer Lloyd – Rules for Classification
and Construction (Edition 2013)

## Slide 6
Scantling Calculations (contd.)
Summary: Thickness of Plates
Items | Dimension (Thickness)
Bottom Shell Plate | 11 mm
Bilge Plate | 10 mm
Side Shell Plate | 11 mm
Keel Plate | 13 mm
Deck Plate | 8 mm

## Slide 7
Scantling Calculations (contd.)
Summary: Bottom Structure
Items | Dimension
Bottom Longitudinal | L-200x150x10
Bottom Center Girder | T-850x550x9
Bottom Side Girder | T-800x450x7
Inner Bottom Longitudinal | L-200x150x9
Floor | T-900x450x8

## Slide 8
Scantling Calculations (contd.)
Summary: Side Structure
Items | Dimension
Main Frame | L-175x100x8
Web Frame | T-250x200x10
Side Longitudinal | L-150x75x8

## Slide 9
Scantling Calculations (contd.)
Summary: Deck Structure
Items | Dimension
Deck Longitudinal | L-100x75x7
Deck Web | T-200x100x10

## Slide 10
Scantling Calculations (contd.)
Summary: Watertight Bulkheads
Items | Dimension
Plate | t = 9 mm
Web | T-200x100x9
Vertical Stiffeners | L-75x50x9
Transverse Stiffeners | L-90x65x7

## Slide 11
Scantling Calculations (contd.)
Summary: Superstructure
Items | Dimension
Top Plate | t = 7 mm
Side Plate | t = 9 mm
Side Frame | L-125x75x7
Web Frame | T-250x175x9
Deck Longitudinal | L-100x75x7

## Slide 12
Midship Section Drawing

## Slide 13
Midship Section Drawing (contd.)

## Slide 14
Midship Section Drawing (contd.)

## Slide 15
Longitudinal Construction Drawing

## Slide 16
Longitudinal Construction Drawing (contd.)

## Slide 17
Longitudinal Construction Drawing (contd.)

## Slide 18
Longitudinal Construction Drawing (contd.)

## Slide 19
Longitudinal Construction Drawing (contd.)

## Slide 20
Longitudinal Construction Drawing (contd.)

## Slide 21
Longitudinal Construction Drawing (contd.)

## Slide 22
Shell Expansion Drawing

## Slide 23
Shell Expansion Drawing (contd.)

## Slide 24
Shell Expansion Drawing (contd.)

## Slide 25
Thank You.

## Slide 26
References
1. Germanischer Lloyd, 13th Edition (GL-13)
2. Illustration of Hull Structures (English/Japanese),
Dr. Hirohiko Emi (Author/Illustrator)