## Slide 1: NAME-338 Ship Design Project & Presentation
Supervised by,
Dr. N. M. Golam Zakaria
Professor,
Dept. of NAME,
BUET.
Presented by,
Touseef Hasan
Student ID: 1812044,
Mehedi Hasan
Student ID: 1712046.

## Slide 2
Owner’s Requirements
Vessel Type: Bulk Carrier
Capacity: 2300 tonnes
Service Speed: 10 knots
Route: Dhaka – Chittagong (Inland)
Route Distance: 315 km (171 nautical miles)

## Slide 3
Principal Particulars
Length Overall
Length between Perpendiculars
Breadth Mld.
Depth Mld.
Draft
Service Speed
CB
: 76.4 m
: 74.4 m
: 13.54 m
: 5.1 m
: 3.85 m
: 10 knots
: 0.79

## Slide 4
List of Contents
Detailed Weight Calculation
Approximate Trim and Stability Calculation
Resistance and Power Calculation
Rudder Design & Steering Arrangement
Propeller Design
Engine Selection & Design of Engine Foundation

## Slide 5
Detailed Weight Calculation
 | Item | Weight (tonnes) | LCG (m) | Moment (t-m) (about aft) | VCG (m) | Moment (t-m) (about keel)
1 | Steel Weight | 640.95 | 29.87 | 19143.08 | 2.40 | 1535.94
2 | Wood & Outfit Weight | 11.49 | 8.19 | 94.07 | 7.09 | 81.47
3 | Machinery Weight | 57.96 | 25.97 | 1505.37 | 3.86 | 223.48
Total Lightship Weight |  | 710.40 | 29.20 | 20742.52 | 2.59 | 1840.88

## Slide 6
Detailed Weight Calculation (contd.)
 | Item | No. | Unit weight (tonnes) | Total weight (tonnes) | LCG (m) | Moment (about midship) | VCG (m) | Moment (about keel)
1 | Main Engine | 2 | 2.39 | 4.78 | 10.8 | 51.62 | 1.65 | 7.89
2 | Gear Box | 2 | 0.72 | 1.44 | 10.6 | 15.26 | 1.6 | 2.30
3 | Generator | 2 | 0.465 | 0.93 | 8.39 | 7.80 | 1.5 | 1.40
4 | Pump | 3 | 0.21 | 0.63 | 8.15 | 5.13 | 1.2 | 0.76
5 | Exhaust and Chimney | 1 | 1.25 | 1.25 | 8.17 | 10.21 | 6 | 7.50
6 | Engine Control Room Equipment | 1 | 3 | 3.00 | 8 | 24.00 | 7.31 | 21.93
7 | Rudder & Steering Arrangement | 2 | 1.96 | 3.92 | 1.62 | 6.35 | 3.63 | 14.23
8 | Anchor & Chain | 3 | 3.06 | 9.18 | 61.6 | 565.49 | 5.5 | 50.49
9 | Bollard, Capstan and other Fittings |  | 4 | 4.00 | 61.68 | 246.72 | 5.5 | 22.00
10 | Propeller, Propeller Shaft | 2 | 1.20 | 2.41 | 1.5 | 3.61 | 0.85 | 2.05
11 | Complete Electrical System |  | 3 | 3.00 | 7 | 21.00 | 5 | 15.00
12 | Hatch Coaming Girder |  | 3 | 3.00 | 34 | 102.00 | 4.5 | 13.50
13 | Complete Piping |  | 2 | 2.00 | 33.5 | 67.00 | 4.3 | 8.60
14 | Windlass | 1 | 1 | 1.00 | 32 | 32.00 | 4.3 | 4.30
15 | Mooring Rope |  |  | 1.00 | 62.5 | 62.50 | 5.7 | 5.70
 |  |  |  | 52.69 |  | 1158.21 |  | 171.94
Machinery Weight

## Slide 7
Detailed Weight Calculation (contd.)
Total Machinery Weight | 57.96 | tonnes
LCG (from aft) | 25.97 | m
VCG (from keel) | 3.86 | m
Machinery Weight (contd.)

## Slide 8
Detailed Weight Calculation (contd.)
Fully Loaded Departure Condition |  |  |  |  |  | 
No. | Item | Weight (tonnes) | LCG (m) | Moment (t-m) (about aft) | VCG (m) | Moment (t-m) (about keel)
1 | Light Ship | 710.40 | 29.20 | 20742.52 | 2.59 | 1840.88
2 | Crew (13) | 0.975 | 8.75 | 8.53 | 5.50 | 5.36
3 | Fuel Oil | 8.85 | 12.34 | 109.21 | 3.07 | 27.17
4 | Lub Oil | 0.07 | 4.60 | 0.32 | 3.00 | 0.21
7 | Fresh Water | 5 | 64.00 | 320.00 | 2.80 | 14.00
9 | Cargo Hold 1 | 450 | 52.67 | 23701.50 | 2.92 | 1314.00
10 | Cargo Hold 2 | 568 | 37.54 | 21322.72 | 2.92 | 1658.56
11 | Cargo Hold 3 | 568 | 21.13 | 12001.84 | 2.92 | 1658.56
Total Weight |  | 2311.30 | 33.84 | 78206.64 | 2.82 | 6518.74

## Slide 9
Detailed Weight Calculation (contd.)
Fully Loaded Arrival Condition |  |  |  |  |  | 
No. | Item | Weight (tonnes) | LCG (m) | Moment (t-m) (about aft) | VCG (m) | Moment (t-m) (about keel)
1 | Light Ship | 710.40 | 29.20 | 20742.52 | 2.59 | 1840.88
2 | Crew (13) | 0.975 | 8.75 | 8.53 | 5.50 | 5.36
3 | Fuel Oil (10%) | 0.885 | 12.34 | 10.92 | 3.07 | 2.72
4 | Lub Oil (10%) | 0.007 | 4.60 | 0.03 | 3.00 | 0.02
7 | Fresh Water (10%) | 0.5 | 64.00 | 32.00 | 2.80 | 1.40
9 | Cargo Hold 1 | 450 | 52.67 | 23701.50 | 2.92 | 1314.00
10 | Cargo Hold 2 | 568 | 37.54 | 21322.72 | 2.92 | 1658.56
11 | Cargo Hold 3 | 568 | 21.13 | 12001.84 | 2.92 | 1658.56
Total Weight |  | 2298.77 | 33.85 | 77820.06 | 2.82 | 6481.50

## Slide 10
Stability Calculations
Condition | Lightship Condition | Arrival Condition | Departure Condition
Angle | GZ(m) | GZ(m) | GZ(m)
0 | 0.000 | 0.000 | 0.000
15 | 0.532 | 0.335 | 0.500
30 | 1.541 | 0.569 | 0.898
45 | 2.313 | 0.703 | 0.974
60 | 2.536 | 0.669 | 0.712
75 | 1.594 | 0.328 | 0.381
90 | -0.248 | -0.040 | -0.060

## Slide 11
Stability Calculations (contd.)
Chart: GZ vs. Angle
| 0 | 15 | 30 | 45 | 60 | 75 | 90
Lightship Condition | 0 | 0.53163 | 1.541 | 2.3134 | 2.5364 | 1.5941 | -0.24829
Lightship Condition

## Slide 12
Stability Calculations (contd.)
Fully Loaded Departure Condition
Chart: GZ vs. Angle
| 0 | 15 | 30 | 45 | 60 | 75 | 90
Departure Condition | 0 | 0.49996 | 0.89838 | 0.97441 | 0.7117 | 0.38136 | -0.060233

## Slide 13
Stability Calculations (contd.)
Fully Loaded Arrival Condition
Chart: GZ vs. Angle
| 0 | 15 | 30 | 45 | 60 | 75 | 90
Arrival Condition | 0 | 0.33469 | 0.56932 | 0.70259 | 0.66863 | 0.32825 | -0.040128

## Slide 14
Properties | IMO value | Lightship Condition | Arrival Condition | Departure Condition | Comment
Area up to 30 degree (m-rad) | ≥ 0.055 | 0.3201 | 0.1665 | 0.2529 | Satisfied
Area up to 40˚ (m-rad) | ≥ 0.09 | 0.7450 | 0.3093 | 0.4740 | Satisfied
Area up to 30˚ - 40˚ (m-rad) | ≥ 0.03 | 0.4250 | 0.1428 | 0.2210 | Satisfied
GZ at 30 degree (m) | ≥ 0.2 | 1.5410 | 0.5693 | 0.8984 | Satisfied
Max. GZ at (degree) | ≥ 30 (preferable) but not ≤ 25 | 45 | 52 | 42 | Satisfied
Initial Metacentric Height (m) | Should not be ≤ 0.15 | 2.3 | 1.4 | 1.9 | Satisfied
Stability Calculations (contd.)

## Slide 15
Trim Calculations
Final Draft of Vessel |  |  | 
 | Draft (aft) | Draft (fore) | Comment
Mean Draft (m) | 3.65 | 3.65 | Trim by Stern
Change in Draft (m) | 0.05 | 0.05 | 
Final Draft (m) | 3.70 | 3.60 | 
Fully Loaded Departure Condition

## Slide 16
Trim Calculations (contd.)
Fully Loaded Arrival Condition
Final Draft of Vessel |  |  | 
 | Draft (aft) | Draft (fore) | Comment
Mean Draft (m) | 3.65 | 3.65 | Trim by Stern
Change in Draft (m) | 0.16 | 0.17 | 
Final Draft (m) | 3.81 | 3.48 | 

## Slide 17
Trim Calculations (contd.)
Lightship Condition
Final Draft of Vessel |  |  | 
 | Draft (aft) | Draft (fore) | Comment
Mean Draft (m) | 3.65 | 3.65 | Trim by Stern
Change in Draft (m) | 0.77 | 0.72 | 
Final Draft (m) | 4.42 | 2.93 | 

## Slide 18
Resistance & Power Calculations
Holtrop & Mennen’s Method

## Slide 19
Resistance & Power Calculations (contd.)
Frictional Resistance | RF | 28.489 | kN
Resistance of Appendages | RAPP | 5.923 | kN
Wave Making and Wave Breaking Resistance | RW | 15.896 | kN
Additional Resistance due to Bulbous Bow | R(B) | 0 | kN
Resistance of Immersed Transom Stern | R(TR) | 0.25 | kN
Model Ship Correlation Resistance | RA | 8.428 | kN
Total Resistance | RT | 58.381 | kN
Resistance Summary

## Slide 20
Resistance & Power Calculations (contd.)
Power Summary
Effective Power | 300.312 | kW
ηo | 0.55 | 
ηd (QPC) | 0.534 | 
Delivered Power | 562.569 | kW
Shaft Power (considering shaft loss of 3.5%) | 582.974 | kW
Power (considering gear box loss of 5%) | 613.656 | kW
Power (considering sea margin of 15%) | 705.704 | kW
Total Brake Power (considering 85% MCR) | 830.241 | kW
Per Engine Brake Power | 415.121 | kW

## Slide 21
Rudder Design & Steering Arrangement
Scantling Summary (Rudder) (DNV – GL 2016)
Used Material | HLS GL F-40 | 
Rudder Area (each) | 2.557 | m2
Mean height | 1.872 | m
Mean breadth | 1.366 | m
Aspect ratio | 1.371 | 
Rudder Force | 41.71 | kN (ahead)
 | 10.92 | kN (astern)
Rudder Torque | 5.696 | kNm (ahead)
 | 6.115 | kNm (astern)
Rudder Stock Diameter | 70 | mm
Coupling Bolt Diameter | 20 | mm
Coupling Flange Thickness | 20 | mm
Rudder Plate Thickness | 8 | mm
Rudder Web Thickness | 7 | mm
Pintle Diameter | 84 | mm
Bearing liners | 8 | mm
NACA Section | 0010 | 

## Slide 22
Rudder Design & Steering Arrangement (contd.)
Rudder Drawing

## Slide 23
Rudder Design & Steering Arrangement (contd.)
Rudder Drawing

## Slide 24
Rudder Design & Steering Arrangement (contd.)
Rudder Drawing

## Slide 25
Rudder Design & Steering Arrangement (contd.)
Rudder Drawing

## Slide 26
Rudder Design & Steering Arrangement (contd.)
Steering Gear

## Slide 27
Rudder Design & Steering Arrangement (contd.)
Steering Gear

## Slide 28
Propeller Design
Cavitation Check
BAR | 0.65
Open water efficiency | 0.55
P/D | 0.91
J | 0.51
Min. BAR (for cavitation) | 0.598

## Slide 29
Propeller Design (contd.)
Propeller Parameters
Number of propellers | 2 | 
Number of blades | 3 | 
BAR | 0.65 | 
Diameter, D | 1.533 | m
P/D | 0.91 | 
Efficiency | 0.55 | 
Propeller speed | 327 | rpm
Pitch, P | 1.395 | m

## Slide 30
Propeller Design (contd.)
Propeller Drawing

## Slide 31
Propeller Design (contd.)
Propeller Drawing

## Slide 32
Engine Selection & Design of Engine Foundation
Selection of Engine and Gear Box
Model | HP | KW | RPM | Rating | Certified By
6M33C750-18 | 649 | 484 | 1800 | P1 | CCS, BV, RS, LR, GL, VR, RINA

## Slide 33
Engine Selection & Design of Engine Foundation (contd.)
Scantling Summary (Engine Room) (DNV – GL 2016)
Plate Floor | 8 | mm
Longitudinal Girder | 8 | mm
Side Girder | 8 | mm
Inner Bottom Plate | 7 | mm
Top Plate (Thickness) | 23 | mm
Top Plate (Width) | 270 | mm
Bottom Plate | 10 | mm
Web Frame | T-200x100x12 | mm
Foundation Bolt (Diameter) | 3 | mm
Foundation Bolt (Spacing) | 70 | mm

## Slide 34
Engine Selection & Design of Engine Foundation (contd.)
Profile View

## Slide 35
Engine Selection & Design of Engine Foundation (contd.)
Plan View

## Slide 36
Engine Selection & Design of Engine Foundation (contd.)

## Slide 37
Engine Selection & Design of Engine Foundation (contd.)

## Slide 38
Engine Selection & Design of Engine Foundation (contd.)

## Slide 39
Engine Selection & Design of Engine Foundation (contd.)
Shafting Arrangement Summary
Shaft Speed | 327 | rpm
Torque | 16 | kNm
Stress | 120 | Nm^-2
Shaft Diameter | 100 | mm
Twisting angle | 4.75 | degrees
Shaft liners | 6 | mm
Coupling | 18 | mm
Shaft bearing max. distance | 2.6 | m
Stern tube bearing (fwd.) | 90 | mm
Stern tube bearing (aft) | 220 | mm
Flange coupling bolt diameter | 38 | mm

## Slide 40
Engine Selection & Design of Engine Foundation (contd.)
SL. NO | DESCRIPTION | MATERIALS | NUMBER OF COMPONENT
1 | Cone nut | M.B. BS | 1
2 | Cone nut securing screw | M.B. BS | 2
3 | Propeller key | M.B. BS | 1
4 | Propeller dia X pitch | M.B. BS | 1
5 | Aft Brg securing screw | M.B. BS | 3
6 | Cover plate securing screw | STEEL BS | 3
7 | Aft locking ring | STEEL BS | 1
8 | Cover plate | STEEL BS | 1
9 | Lock ring securing screw | STEEL BS | 3
10 | FWD locking ring | STEEL BS | 1
11 | Rubber bearing |  | 
12 | Sterntube | STEEL BS | 1
13 | Tailshaft |  | 1
14 | gland housing | G.M. BS | 1
15 | FWD bearing | G.M. BS | 1
16 | Greasy packing | GRAPHITED ASBESTOS | 3 turns
17 | Gland ring | G.M. BS | 1
18 | Gland studs and nuts | M.B. BS | 2
19 | Coupling key | STEEL BS | 1
20 | Half coupling | STEEL BS | 1
21 | Backing washer | STEEL BS | 1
22 | Locking nut | STEEL En7 BS | 1
23 | Sealing ring | BS | 1
24 | Fwd brg securing screw | M.B. BS | 1
25 | Bearing lock ring | STEEL BS | 1
Shafting Arrangement Summary

## Slide 41
Engine Selection & Design of Engine Foundation (contd.)
Shafting Arrangement Drawing

## Slide 42
Thank You.